PHYC 3540

Summary

- Propagation of light

  - History, wave vs. particle picture

  - Fermats Principle – actual path is that for which the OPL is an extremum

  - Huygen’s principle – every point on wavefront acts as a source

    - Large aperture (>>() – rectilinear propagation  (Geometric optics)

    - Small aperture () – spreading of wavefront (Diffraction)

  - Wavefronts, Rays – Laws of reflection and refraction (Snels law)

- Geometric Optics

  - Imaging – Cartesian surfaces, Paraxial ray approximation

  - Refraction at a Spherical interface

  - Thin lens

  - Principal Planes (H,H’)

    - Used to represent any optical element or system and are located such that the system images an object according to:

    - The principal planes used to represent a spherical interface (or thin lens) must coincide at the interface (or centre of the thin lens).

  - Combination of two systems

    - Power of combined system 					where,   and

    - The location of H, H’ are determined with respect to H1 and H2’ as follows:

  - Matrix methods in paraxial optics

    - Matrices

Translation matrix

Refraction matrix

Reflection matrix

Thin lens matrix

    - Cardinal point locations

  - Stops in optical systems

    - Aperture stop

      - Element that limits the bundle of rays (and hence light gathering power or speed) collected by optical system

      - Is that element whose entrance pupil subtends the smallest angle at the object point in question

      - Exit pupil is the image of the aperture stop in all elements following it

      - Entrance pupil is the image of the aperture stop in all elements preceding it

    - Field stop

      - Element of the optical system that limits the field of view

      - That element whose entrance window subtends the smallest angle at the centre of the entrance pupil

      - Exit window is the image of the field stop in all elements following it.

      - Entrance window is the image of the field stop in all elements preceding it

    - Chief ray, marginal rays – definition of edge of field of view

    - Angular field of view

      - Image space – angle formed by the entrance window as viewed from the centre of the entrance pupil

      - Object space – angle formed by the exit window as viewed from the centre of the exit pupil

  - Applications

    - Cameras (aperture settings (f#), exposure, telephoto lens)

    - Human eye – myopia, hyperopia

    - Hand magnifiers, eyepieces, compound microscope

    - Telescope, binoculars

- Physical optics (wave properties are important)

  - Wave equation – plane waves, spherical waves, cylindrical waves

  - Amplitude reflection and transmission co-efficients

  - Electromagnetic waves (E ( B; E, B in phase, speed c/n)

    - Irradiance

    - Transmittance

    - Reflectance (1(2)

  - Interference

    - Two source interference

      - Irradiance

      - If (1 = (2 and I1=I2=Io there are maxima located at,

      - Examples

        - Double slit, Lloyds mirror, radio towers

        - Dielectric layers, e.g. Haidinger bands, fringes of equal thickness observed in oil films, air wedges

        - Antireflection coatings

        - Newton’s rings

    - Multiple beam interference (coated dielectric layers)

      - Transmitted irradiance										where,  and n, (’  pertain to the dielectric layer.

        - Irradiance maxima occur when

      - Fabry-Perot Interferometer

        - Finesse =

        - Free spectral range

        - Fringe width

        - Spectral Resolution

  - Diffraction

    - Fresnel–Kirchoff diffraction formula	(Mathematical statement of Huygen’s principle)													where,

    - Fraunhofer limit (plane waves)						diffraction integral reduces to

      - Single slit (width b)							   where, 			  when

      - Circular aperture (diameter do = 2ao)						where, ( = kaosin(					when  			Airy disc; Spatial resolution of optical devices; focussing limit

      - N slits (width b, separation a)						 where, 		Principal maxima when

      - Diffraction gratings							Grating dispersion						Spectral resolution

  - Polarization

    - Jones vector for polarization							General 							Vertical       Horizontal 					Linearly polarized at an angle (α,  			Left Circularly polarized (i.e. counterclockwise)		Right Circularly polarized 	(i.e. clockwise)		Left Elliptically polarized 			Right Elliptically polarized 		where, 			and the angle of inclination, α, of the ellipse is given by

    - Jones matrices for optical elements

      - Linear polarizer (Transmission axis at an angle ( wrt x-axis)

      - Phase retarders							In general,  where, (x and (y represent the advance in phase of the components

        - Quarter wave plate (|(y - (x| = (/2)				  Slow axis vertical			 Slow axis horizontal

        - Half wave plate (|(y - (x| = ()					  Slow axis vertical			 Slow axis horizontal

      - Rotator (light polarized at an angle ( is rotated by an angle ()

  - Holography

    - Hologram																	where, R – reference wave, O – object wave, I - intensity

    - Reconstructed wave					where, t – transmission, first term – direct wave, second term – conjugate wave, third term – object wave

# Text boxes

R

s

s'

n

n'

s

s'

n

n'

F

F’

s'

s

f'

f

n'

n

H’

H

f'

f

s'

s

n2

n

H’

n'

H

H2’

H2

H1’

H1

P

r

r'

n